## Slide 1: ISO/IEC 17025: 2005 CAR Administrator Training
February 15, 2012, Rev. 5
For questions or comments on the content, please contact Cheryl Allison

## Slide 2: Course Objective
Upon completion, CAR Administrators will:
  Understand the intent of the ISO 17025 Standard
  Be able to determine if a CAR response meets or violates an ISO 17025 standard requirement
  Understand how to locate ISO 17025 compliance documentation and records in various UL databases
Notes: CAR Administrators do not need to be standards experts, but need only to be familiar with the intent and format of the Standards. (2) Being able to ask the rights questions and knowing where to find information in the standards is the intent of this course (3) Even the best CAR Owners may unknowingly violate a standard requirement, which is why CAR Administrators must be able to “think with standard” when reviewing corrective action plans (4) While IQA Auditors are always available to assist in difficult standard interpretation issues, many standard related questions are straight forward enough to be handled directly by the CAR Administrator (5) Location of ISO 17025 compliance documentation – Instructor should determine the best way to do this. For example, database identification and use could be discussed after each clause of the standard, or it may be preferable to complete the standards training first, and then later review the applicable databases in a focused session. This may allow a better focus on the standards related concepts.

## Slide 3: Agenda
What is ISO 17025
Application of ISO 17025 to the CAR Administrator function
  Location of ISO 17025 compliance documentation and records
  Workshop
Notes: We begin with a 30,000 foot view of ISO 17025, and then explore the intent of each ISO 17025 requirement. Next, we introduce a process for CAR Administrators to follow to ensure that corrective action plans do not violate ISO 17025 requirements. Finally, we apply what we have learned today in a group workshop

## Slide 4: What is ISO 17025?
ISO 17025 was written by the International Organization for Standardization (ISO)
      Based upon international consensus among experts in the field
ISO 17025 provides generic and flexible requirements
      E.g., ISO 17025 requires control of documentation, but does not specify the specific documentation control methods/techniques
Notes: (1) The goal of the ISO Organization is STANDARIZATION to facilitate global harmonization of technical requirements (2) The generic and FLEXIBLE nature of ISO standards are the keys to ensuing that large and small companies alike can use the standards (3) Give students an idea of how tough it would be to meet the requirements of many standards from many different customers as opposed to one internationally accepted standard

## Slide 5: What is ISO 17025?
ISO 17025 – “General requirements for the competence of testing and calibration laboratories”
  Standard used by testing and calibration laboratories
  Contains two main sections
    Management Requirements
        Operation and effectiveness of laboratory quality management system
    Technical Requirements
        Control the factors of the correctness and reliability of the tests and/or calibrations (5.1 of 17025)
Notes: (1) The term “General” in the title further illustrates that ISO 17025 is a generic and flexible standard (2) ISO 17025 stresses competence, where ISO 9001 for example places an emphasis on customer satisfaction

## Slide 6: Intent of ISO 17025
To facilitate cooperation between laboratories and other bodies, and assist in the exchange of information and experience, and in the harmonization of standards and procedures, by defining the general requirement of the competence of testing and calibration laboratories (Introduction of 17025)
Notes: Through the effective management of laboratory processes, accurate test / calibration results are enhanced.

## Slide 7: ISO 17025 Requires
The effective implementation of processes to accomplish each standard requirement
Processes are interrelated work activities
Competent personnel
Clear assignment of the authority, responsibility and interrelationship of laboratory personnel
Notes: (1) Provide a brief overview of process theory / management (2) Re-enforce that 17025 provides considerable focus upon competency (3) Emphasize that without defined responsibility, the probability of errors increase as commitment / accountability is absent

## Slide 8: ISO 17025 Requires
Documented procedures where required by the standard and internal procedures
    Not all processes are required to be documented in procedure, e.g., training records, automated tools, templates and forms may be used in lieu of documented procedures
Records where required by the standard and internal procedures
    Records are not required for every standard requirement or process/sub-process in an organization
    Technical records must facilitate an effective audit trail and enable test conditions to be repeated
Notes: (1) PROCESSES drive the laboratory management system, not just documented procedures. (2) Records provide evidence that laboratory processes are effectively implemented

## Slide 9: Why is ISO 17025 Important to UL?
UL bases certification decisions upon the results of Laboratory Testing
  Accurate results are enhanced through compliance to ISO 17025
UL Certification system is accredited to Guide 65. Compliance to 17025 is one way we satisfy certain Guide 65 requirements (Only a few UL labs are accredited according to 17025)
  Critical “credential” to demonstrate UL’s competence to current and potential customers
Notes: (1) ISO 17025 makes UL better internally and is demanded externally. (2) We can be as lean as we want, but without accreditation the UL business may vanish!

## Slide 10: ISO 17025 Clause 4.1 – Management Requirements - Organization
Clause Intent
  The laboratory is organized such that managerial and technical personnel may effectively carry out their duties
Clause Requirement Example
  The responsibility, authority and interrelationships of all personnel who manage, perform or verify work affecting the quality of the tests and/or calibrations shall be defined
    Organization chart
    Job descriptions
    Responsibilities specified in policies, procedures, work instructions
Notes: Note for all clause slides to follow: Clause requirement examples are presented for all ISO 17025 requirements to further illustrate the intent of each clause. These examples are not verbatim requirements, but have been summarized for clarity. Remember that this is NOT a clause interpretation course like an auditor would attend. With this in mind, do not encourage students to follow along in the standard and ask specific detailed clause based questions. They will have an opportunity to get into the standard during the workshop later in the course
UL IMPLEMENTATION SLIDES TO FOLLOW- This training has not attempted to include all applicable documentation for each 17025 clause. Instead, “main” or “primary” documentation was selected to make teaching points clear, and not overwhelm the students with many procedure references.
Management is the essential element that determines the success of any management system. ISO 17025 not only asks for management support, but requires active management participation.

## Slide 11: ISO 17025 Clause 4.1 – Management Requirements - Organization
UL Implementation
Organizational Chart Policy, 00-HR-P0051: Defines the policy/process for the creation and maintenance of organization charts
Standards of Business Conduct, 00-LE-P0001: Requires that management, staff and sub-contractors are free from any undue internal and external commercial, financial and other pressures and influences that could adversely affect quality
Global Policy and Process Owners Matrix 00-QA-P0031 - Identifies global policy and process owners

## Slide 12: ISO 17025 Clause 4.2 – Management Requirements – Management System
Clause Intent
  The laboratory shall effectively implement a documented management system
Clause Requirement Example
  Management system documentation shall include
    Quality policy
    Quality objectives
    Quality manual
    System documentation (polices, procedures, work instructions, etc.)
Notes: Explain that ISO 17025 is a system based standard, and that effective operations of systems provides confidence in accurate and repeatable results. Contrast the system approach against a company that uses “tribal knowledge” (2) Explain how the policy is connected to objective and system documentation. (3) Explain the concept that quality manuals are typically “road maps” to the lab management system as opposed to the entire system as was the case in the 1980 – early 1990s quality manuals.

## Slide 13: ISO 17025 Clause 4.2 – Management Requirements – Management System
UL Implementation
UL Vision, Mission & Values: Defines the reasons why UL exists
UL Quality Policy: Describes UL’s policy for quality
UL Global Quality Manual, 00-QA-P0001: Describes the UL quality management system
Laboratory Objectives: Defines and Reviews specific goals during the Management Review 00-LC-P0040
All Laboratory Process Documentation (Policies, LPGs, SOPs, etc.): Comprise UL’s documented management system

## Slide 14: ISO 17025 Clause 4.3 – Document Control
Clause Intent
  Management system documentation is controlled
    Policies, procedures, laboratory work instructions, specifications, calibration tables, drawings, etc. These may be on various media, including hard copy, electronic, digital, analog, photographic or written.
Clause Requirement Example
  Management system documents shall be
    Reviewed and approved
    Made available where needed
    Removed when obsolete
Notes: Make clear the difference between a record and a document (2) Highlight that documents are not just SOPs but may be the items noted above

## Slide 15: ISO 17025 Clause 4.3 – Document Control
UL Implementation
Document Management SOP, 00-QA-S0003: Ddefines the minimum format, structure, content and electronic publishing process for policies, standard operating procedures (SOPs), forms and work instructions
Standard Operating Procedure for Developing and Maintaining Laboratory Procedure Guides - 00-LC-S0002: Establishes a uniform method for developing and maintaining Laboratory Procedure Guides (LPGs)

## Slide 16: ISO 17025 Clause 4.3 – Document Control
UL Implementation, cont.
Global Form Management Process – 00-QA-S0026 Describes the process for creating or modifying a CCN related Global Form, which resides within the ePublisher portion of the GFL.

## Slide 17: ISO 17025 Clause 4.4 – Review of Requests, Tenders and Contracts
Clause Intent
  Capability exists to meet customer requirements before accepting work
Clause Requirement Example
  The laboratory shall ensure
    Customer requirements are adequately defined, documented and understood
    The laboratory has the capability and resources to meet the requirements
Notes: Stress that this clause is about not promising more than you can deliver, and covers technical requirements as well as terms & conditions.
Contract review deals with the CAS and Lab interface., as the UL LAB does not interface with the external UL customer during the contract review phase

## Slide 18: ISO 17025 Clause 4.4 – Review of Requests, Tenders and Contracts
UL Implementation
When testing is part of a product certification program, the customer is the UL staff member responsible for the conduct of the product certification program
When testing is not part of a product certification program (e.g., commercial testing), the customer is the external entity entering into a contract
Notes: Explain the concept of the customer as applicable to the UL Laboratories

## Slide 19: ISO 17025 Clause 4.4 – Review of Requests, Tenders and Contracts
UL Implementation, cont.
Standard Operating Procedure - Project Startup Process, 00-SA-S0026: Establishes a standard operating procedure for quoting and quote Acceptance
Project Handling Process (E-Production), 00-OP-S0044: Section 9.11 defines the detailed assessment of customer requests, quotations, sample requirements and proposed test programs

## Slide 20: ISO 17025 Clause 4.5 – Subcontracting of Tests and Calibrations
Clause Intent
  Subcontracted work is conducted by competent subcontractors in accordance with ISO 17025
Clause Requirement Example
  The laboratory is responsible to the customer for the subcontractor’s work
Notes: Stress that the Lab is responsible regardless if a sub-contractor is used or not. (2) Explain how the integrity of 17025 is compromised if sub-contractors do not perform work in accordance with ISO 17025 (3) Explain that UL Mark subcontracting is addressed under DAP

## Slide 21: ISO 17025 Clause 4.5 – Subcontracting of Tests and Calibrations
UL Implementation
Laboratory does not subcontract testing under product certification.

## Slide 22: ISO 17025 Clause 4.5 – Subcontracting of Tests and Calibrations
UL Implementation
CAS subcontracts testing under the Data Acceptance Program for UL Mark Program. (Other Mark programs have its own process for accepting external test data)
  Data Recording, Reporting and Related Requirements for DAP Clients, 00-OP-C0025: UL’s requirements for data recording and reporting for the Data Acceptance Program (DAP)
  DAP Acceptance Program Assessment Procedure, 00-OP-S0056: Provides staff with a uniform process for conducting the assessment that will determine an external laboratories capability to perform tests independently under DAP

## Slide 23: ISO 17025 Clause 4.6 – Purchasing Services and Supplies
Clause Intent
  To ensure external services and supplies not reduce the quality of tests and/or calibrations
Clause Requirement Example
  The laboratory shall have a policy and procedure for the selection and purchasing of services and supplies it uses that affect the quality of the tests and/or calibrations
Notes: Explain the impact of poor sub-contractor performance, and why proactive supplier management is a superior model to using inspection alone. (2) Provide examples of services and supplies that would be included and would not be included

## Slide 24: ISO 17025 Clause 4.6 – Purchasing Services and Supplies
UL Implementation
Global Policy for the Use of Calibration Vendors, 00-LC-P0026: Provide a global policy for the selection, use and related policies for the selection of calibration vendors
Non-Accredited Calibration Vendor Survey, 00-LC-F0037: Survey used to confirm the competency of calibration Vendor, when vendor is not accredited for the service provided

## Slide 25: ISO 17025 Clause 4.6 – Purchasing Services and Supplies
UL Implementation, cont.
Purchase, Receipt, Verification and Storage of Critical Laboratory Consumables, 00-L0-S0409: Describes the process for purchase, receipt, verification and storage of critical laboratory consumables

## Slide 26: ISO 17025 Clause 4.7 – Service to the Customer
Clause Intent
  To ensure customer friendly service.
Clause Requirement Example
  The laboratory shall seek feedback, both positive and negative, from its customers. The feedback shall be used and analyzed to improve the management system, testing and calibration activities and customer service.
Notes: Explain that this a proactive clause, and just reacting to customer inquiries and complaints is not enough.
Note that UL LABs do not interface directly with external customers. Positive and negative feedback between CAS and UL laboratories is inherent in the interaction between the two entities. There is no need for the laboratory to formally seek this feedback in this situation.

## Slide 27: ISO 17025 Clause 4.7 – Service to the Customer
UL Implementation
External customers may witness laboratory testing and visit UL to tour facilities
Customer feedback is solicited via surveys, forums, roundtable discussions, and other formal venues that involve manufacturers, industry officials, and authorities. Analysis is conducted annually. Goal is set for improving Net Promoter Score (indication of UL customers likelihood to recommend UL. A key factor in measuring our overall performance and customer satisfaction)

## Slide 28: ISO 17025 Clause 4.8 – Complaints
Clause Intent
  Effectively resolve complaints from customers or other parties
Clause Requirement Example
  Records shall be maintained of all complaints and of the investigations and corrective actions taken
Notes: Explain that each complaint must be addressed, and that a formal corrective action for each complaint may or may not be appropriate. (2) “Other parties” may include accreditation bodies, regulators, etc.

## Slide 29: ISO 17025 Clause 4.8 – Complaints
UL Implementation
Standard Operating Procedures for Handling Customer Complaints, 00-CS-S0012: Provides a standardized approach to handling and addressing customer complaints, which includes guidance for categorizing, tracking, and analyzing
Global Laboratory Complaints Policy, 00-LC-P0046: Provides guidance to the UL Global Laboratory Testing Organization (TO) for the management of internally generated complaints

## Slide 30: ISO 17025 Clause 4.8 – Complaints
UL Implementation, cont.
Corrective Action Request Process, 00-QA-S0006: Describes the process for initiating and managing Corrective Action Requests (CARs)
Appeals and disputes are addressed per policy/procedure associated with each particular program
Notes: Technical appeals are addressed under Guide 65

## Slide 31: ISO 17025 Clause 4.9 – Control of Nonconforming Testing and/or Calibration Work
Clause Intent
  Appropriate actions are taken after nonconforming work is found.
Clause Requirement Example
  Responsibilities are defined and actions taken when nonconforming work is identified
Notes: A typical example is conducting testing in conflict with a test SOP
(2) Explain the connection to the CAR process, and that not every nonconformity must result in a CAR
(3) Explain the trace back process and the connection to the CAR process. Note that every nonconformity does not necessarily result in a CAR
(4) Key point is to identify who is responsible for stopping work
(5) A test failure is NOT nonconforming if the test was done correctly

## Slide 32: ISO 17025 Clause 4.9 – Control of Nonconforming Testing and/or Calibration Work
UL Implementation
Global Laboratory Non-conforming Test or Calibration Work Policy, 00-LC-P0048: Provides the responsibilities and authorities for the management of nonconforming work and the actions to be taken when nonconforming work is identified
Global Laboratory Calibration Policy, 00-LC-P0028: Provides the core requirements for calibration related processes for the UL Global Testing Organization including the process to control the work when equipment is found out of calibration.

## Slide 33: ISO 17025 Clause 4.10 – Improvement
Clause Intent
  The effectiveness of the laboratory management system must continually improve
Clause Requirement Example
  The laboratory shall continually improve the effectiveness of its management system through the use of the quality policy, quality objectives, audit results, analysis of data, corrective and preventive actions, and management review
Notes: A typical example is the improvement of previously identified negative trends (2) Explain that improvement may occur in any area of the lab operations

## Slide 34: ISO 17025 Clause 4.10 – Improvement
UL Implementation
Improvements identified in accordance with the Global Laboratory Management Review Policy, 00-LC-P0040
UL Global Quality Manual, 00-QA-P0001: Describes UL’s approach to improvement
  Initiatives led by Business Excellence (Lean projects Kaizen projects)
  Specific laboratory initiatives
  Management Review

## Slide 35: ISO 17025 Clause 4.11 – Corrective Action
Clause Intent
  Prevent the recurrence of nonconforming work or departures from procedures
Clause Requirement Example
  The laboratory shall monitor the results to ensure that the corrective actions taken have been effective
UL Implementation
Corrective Action Request Process, 00-QA-S0006: Describes the process for initiating and managing quality management system related Corrective Action Requests (CARs)
Notes: The key here is that nonconformities do not recur (2) Addressing the true cause of the nonconformity and carefully evaluating the effective implementation of corrective actions taken are central points to cover (3) May wish to give examples of symptom vs. cause and techniques for evaluating effective implementation based on your experience

## Slide 36: ISO 17025 Clause 4.12 – Preventive Action
Clause Intent
  Prevent the occurrence of nonconforming work and implement needed improvements
Clause Requirement Example
  Procedures for preventive actions shall include the initiation of such actions and the application of controls to ensure that they are effective
Notes: Explain that preventive action is a pro-active process rather than a reaction to the identification of problems or complaints (2) May wish to cites examples of how management review results, data analysis, Lean Sigma activities, FSM etc. could be used in the preventive action process

## Slide 37: ISO 17025 Clause 4.12 – Preventive Action
UL Implementation
Improvements opportunity reviewed in accordance with the Global Laboratory Management Review Policy, 00-LC-P0040
UL Global Quality Manual, 00-QA-P0001 : Describes UL’s approach to Preventative action
  Initiatives led by Business Excellence (Lean projects Kaizen projects)
  Management Review
Notes: Make clear the difference between a CA and PA
Ask for an example of a PA in you lab

## Slide 38: ISO 17025 Clause 4.13 – Control of Records
Clause Intent
  Manage entire life cycle (receipt, retention and disposal) and generation of records
Clause Requirement Example
  All records shall be legible and shall be stored and retained in such a way that they are readily retrievable
  When mistakes occur in records, each mistake shall be crossed out, not erased, made illegible or deleted, and the correct value entered alongside
Notes: Review difference between a document and a record (2) Provide examples that illustrate records may include a wide variety of media (completed forms, contracts, work sheets, work notes, control graphs, external and internal test reports, calibration certificates, etc.)
NOTE: Laboratory compliance control of records policy soon to be released in 00-LC-P0047. Watch document control for future posting.

## Slide 39: ISO 17025 Clause 4.13 – Control of Records
UL Implementation
Global Records Policy, 00-QA-P0026: Defines the requirements for establishing, maintaining, controlling and the disposition of records needed to provide evidence of conformity to requirements and the effective operation of UL’s management system
Data Recording, Reporting and Related Requirements, 00-LC-S0258: Provides product testing staff with documented data recording procedures

## Slide 40: ISO 17025 Clause 4.14 – Internal Audits
Clause Intent
  Verify that operations continue to comply with the requirements of the ISO 17025 quality management system
Clause Requirement Example
  The internal audit program shall address all elements of the quality management system, including the testing and/or calibration activities.
Notes: Explain how internal audits play a key role in the “self regulation” of the management system – Speak to possible uses of the IQA result data (2) Emphasize the relationship to the corrective action system

## Slide 41: ISO 17025 Clause 4.14 – Internal Audits
UL Implementation
Internal Audits Procedure, 00-QA-S0004: Describes the planning, preparation, performance, reporting and management of internal audits
US Laboratory Technical Audits, 80-LC-S0026: Describes the process for conducting peer technical audits in the laboratory
Notes: Explain how internal audits play a key role in the “self regulation” of the management system – Speak to possible uses of the IQA result data (2) Emphasize the relationship to the corrective action system

## Slide 42: ISO 17025 Clause 4.15 – Management Reviews
Clause Intent
  To ensure the continuing suitability and effectiveness of the management system
Clause Requirement Example
  Top management shall periodically conduct a review of the laboratory's management system to ensure their continuing suitability and effectiveness, and to introduce necessary changes or improvements

## Slide 43: ISO 17025 Clause 4.15 – Management Reviews
UL Implementation
Global Laboratory Management Review Policy, 00-LC-P0040: Describes the requirements for laboratory management reviews for the UL Global Testing Organization (TO)
Notes: Explain the critical role Top Management plays in the management system (2) Explain how management review plays a key role in the “self regulation” of the management system - Speak to possible uses of the Management Review result data

## Slide 44: ISO 17025 Clause 5.1 – Technical Requirements
Clause Intent
  Identify the input for Testing/ Calibration process.
Clause Requirement Example
  The extent to which the factors contribute to the total uncertainty of measurement differs considerably between (types of) tests and between (types of) calibrations. The laboratory shall take account of these factors in developing test and calibration methods and procedures, in the training and qualification of personnel, and in the selection and calibration of the equipment it uses.
Notes: Explain some of the factors that contribute to correct test results (human factors, environment, sampling, etc.) and the importance of considering all appropriate factors prior to developing a test plan. Explain that this clause is typically not audited by itself, but findings are written at the specific clause level. For example problems with correctness of test would be written against 5.4, Equipment 5.5, Sampling 5.7, etc.

## Slide 45: ISO 17025 Clause 5.1 – Technical Requirements
UL Implementation
UL has documented policy/procedures for all factors identified in Clause 5.1

## Slide 46: ISO 17025 Clause 5.2 – Personnel
Clause Intent
  Personnel who affect the quality of testing and / or calibrations must be competent
Clause Requirement Example
  The laboratory shall maintain records of the relevant authorization(s),competence, educational and professional qualifications, training, skills and experience of all technical personnel
Notes: Reinforce the key role that competence plays in ISO 17025 (2) Discuss the difference between training, education and experience vs. competence

## Slide 47: ISO 17025 Clause 5.2 – Personnel
UL Implementation
UL’s documented competency criteria (held at local levels)
  Technical Competency Requirements for Evaluation Staff - Laboratory 00-TC-G0050: Contains the minimum competency requirements for Laboratory evaluation staff (Laboratory Technicians; “Level 1’s”).
      Technical Competency Database
Notes: NOTE – Documented L1 Competency Criteria is soon to be released in 00-LC-S0328 – Watch document control for future posting

## Slide 48: ISO 17025 Clause 5.3 - Accommodation and Environmental Condition
Clause Intent
  Laboratory environmental conditions (temperature, humidity, lighting, etc.) must be controlled to ensure accurate test results
Clause Requirements Example
  The laboratory shall monitor, control and record environmental conditions as required by the relevant specifications and methods
Notes: Reinforce the key role that environmental conditions play in accurate test results. Provide brief examples from your experience if desired (2) Explain that appropriate environmental conditions are typically stated in test methods, Standards, Lab SOPs, etc.

## Slide 49: ISO 17025 Clause 5.3 - Accommodation and Environmental Condition
UL Implementation
Global Laboratory Accommodation and Environmental Conditions Policy, 00-LC-P0025: Describes the accommodation and environmental condition requirements for testing
Global Laboratory Housekeeping Policy, 00-LC-P0038: Establishes a global standard for housekeeping in laboratory areas
Notes: We monitor lab conditions 24/7 & keep a record

## Slide 50: ISO 17025 Clause 5.4 –Test and Calibration Methods/Methods Validation
Clause Intent
  The laboratory shall use appropriate methods and procedures to ensure the validity of all tests and/or calibrations
Clause Requirements Example
  The laboratory shall have instructions on the use and operation of all relevant equipment, and on the handling and preparation of items for testing and/or calibration
Notes: (1) Reinforce the important role that documented test methods play in accurate and repeatable test results – Provide examples from your experience where testing was compromised by an inappropriate test method (2) Identify the link to document control

## Slide 51: ISO 17025 Clause 5.4 –Test and Calibration Methods/Methods Validation
UL Implementation
Test and Calibration Methods Policy, 00-LC-P0049: Provides direction to UL staff on the test and calibration method policy
Estimating Uncertainty of Measurement, 00-LC-S0278: Provides technical staff with a uniform process for performing uncertainty of measurement analysis
Global Laboratory Software Verification and Validation SOP, 00-LC-S0401: Establishes requirements for the validation of software which affects the test data/results.

## Slide 52: ISO 17025 Clause 5.5 – Equipment
Clause Intent
  Equipment used for testing, calibration and sampling shall be capable of achieving the accuracy required and shall comply with specifications relevant to the tests and/or calibrations concerned.
Clause Requirements Example
  Before being placed into service, equipment (including that used for sampling) shall be calibrated or checked to establish that it meets the laboratory's specification requirements and complies with the relevant standard
Notes: Reinforce the important role that proper equipment plays in obtaining accurate and repeatable test results
Provide examples from your experience of improper equipment that affected test results

## Slide 53: ISO 17025 Clause 5.5 – Equipment
UL Implementation
Global Laboratory Equipment Policy, 00-LC-P0031: Provides guidelines and requirements to ensure that equipment and software is capable of achieving the accuracy required and complies with relevant specifications. Also addresses equipment maintenance

## Slide 54: ISO 17025 Clause 5.6 – Measurement Traceability
Clause Intent
  All equipment used for tests and/or calibrations having a significant effect on the validity of the results shall be calibrated
Clause Requirements Example
  The program for calibration of equipment shall ensure that calibrations and measurements are traceable to the International System of Units (i.e., SI) NIST and other national metrology institution may have the standard which is not SI based.
Notes: Explain how the unbroken chain from a gage to a standard is established, and what NIST is (2) Explain that calibrated equipment applies only to equipment having an effect on the accuracy or validity of the result of the test (3) Elaborate on system of units applicable to your country (NIST, JIS, etc.)

## Slide 55: ISO 17025 Clause 5.6 – Measurement Traceability
UL Implementation
Global Laboratory Calibration Policy, 00-LC-P0028: Provides the core requirements for calibration related processes for the UL Global Testing Organization
Global Laboratory Equipment Policy, 00-LC-P0031 : Addresses measurement traceability

## Slide 56: ISO 17025 Clause 5.7 – Sampling
Clause Intent
  Sampling plans must ensure the validity of test and calibration results
Clause Requirements Example
  The laboratory shall have procedures for recording relevant data and operations relating to sampling
UL Implementation
Global Laboratory Sampling Policy, 00-LC-P0039: Describes the UL global TO policy for sampling
Notes: Re-enforce the critical role sampling plays in obtaining accurate test results. (2) Provide examples of how inadequate sampling plans could adversely effect test results (3) Most UL sites do not perform sampling – Water group does

## Slide 57: ISO 17025 Clause 5.8 – Handling of Test and Calibration Items
Clause Intent
  Proper handling ensures accurately reporting test and calibration results and the interests of the laboratory and the customer protected.
Clause Requirements Example
  The laboratory shall have procedures to avoid deterioration, loss, or damage to the test or calibration item during storage, handling and preparation
Notes: (1) Review the role that proper handling plays in obtaining accurate test results. (2) Provide examples of how inadequate sampling plans could adversely affect test results
Provide examples of how careless handling could effect test results

## Slide 58: ISO 17025 Clause 5.8 – Handling of Test and Calibration Items
UL Implementation
Global Sample Policy, 00-OP-P0400: Describes the requirements for the handling, storage, and disposition of samples, collectively known as sample management
Notes: Maintain ID from receipt to test to disposal
Explain Sample Tracking System – It is not mandatory – LIMs is suppose to take over

## Slide 59: ISO 17025 Clause 5.9 – Assuring the Quality of Test and Calibration Results
Clause Intent
  To assure the validity of tests and calibrations through comparing test results
Clause Requirements Example
  Quality control data shall be analyzed, and where outside of pre-defined criteria, action taken
Notes: Provide examples of monitoring methods such as proficiency-testing programs, retesting or recalibration of retained items, interlaboratory comparison or correlation studies

## Slide 60: ISO 17025 Clause 5.9 – Assuring the Quality of Test and Calibration Results
UL Implementation
Proficiency Testing, 00-LC-P0029: Defines the roles, responsibilities and processes for the design and completion of proficiency testing
Global Laboratory Calibration Policy, 00-LC-P0028: Provides the core requirements for calibration related processes for the UL Global Testing Organization
Global Laboratory Management Review Policy, 00-LC-P0040: Describes the requirements for laboratory management reviews for the UL Global Testing Organization (TO)

## Slide 61: ISO 17025 Clause 5.10 – Reporting the Results
Clause Intent
  The results of testing and calibration activity shall be reported accurately and in accordance with specified methods
Clause Requirements Example
  The results shall be reported and include all the information requested by the customer and necessary for the interpretation of the test or calibration results
Notes: (1) Explain the general type of information contained in a test report and calibration certificate.
(2) Explain that technical records must facilitate effective audit trail and enable test conditions to be repeated

## Slide 62: ISO 17025 Clause 5.10 – Reporting the Results
UL Implementation
Data Recording, Reporting and Related Requirements, 00-LC-S0258: Provides product testing staff with documented data recording procedures
Form Datasheet Requirements, 00-LO-S0405: Provides requirements for the creation or revision of electronic form datasheets or datasheet packages that can then be used to develop electronic or paper datasheets.
Global Laboratory Calibration Policy, 00-LC-P0028: Provides the core requirements for calibration related processes for the UL Global Testing Organization
Notes: UL does not need to meet all 5.10.2 requirements, as CAS is the customer for the Lab, and the data sheets are all that CAS needs

## Slide 63: Application of ISO 17025 to the CAR Administrator Function
CAR Administrators must ensure that corrective action plans comply with ISO 17025 standard requirements

## Slide 64: Corrective Action Plan Review
Understand the linkage between the nonconformity statement and the ISO clause violated
  If an ISO standard is not identified in the CAR, match the nonconformity statement to the most appropriate ISO clause(s)
  Verify the linkage between the corrective action plan and the violated ISO Clause(s) – there must be a match
Notes: (1) Understanding the linkage between the nonconformity statement and the ISO clause violated provides the CAR Admin a “working understanding” of the issue at hand. (2) If a match does not exist between the corrective action plan and the violated ISO clause, it is likely that the owner is missing key elements needed in the corrective action plan (3) Cross reference table for all ISO Standards 00-QA-J0030 (4) Remember that responses must also meet UL requirements in addition to ISO Standard requirements

## Slide 65: Corrective Action Plan Review, cont.
  Establish “links” to other applicable ISO clauses
    Document control and control of records are impacted by most corrective action plans
  Verify that the corrective action plan does not violate ISO clause requirements
Notes: (1) It is very common that corrective action plans impact other ISO clauses. (2) After all appropriate ISO clause linkages have been identified, ensure that the corrective action plan does not violate and specific clause requirements. For example, an Owner may not include a new SOP in document control, may not keep required records, etc.

## Slide 66: Workshop
In your teams, discuss and determine if the case studies meet the appropriate ISO 17025 standard requirements
Appoint a group leader to report team conclusions

## Slide 67: End

## Slide 68: Revision History
Rev 5 – February 15, 2012 – Added document links. Removed CITS reference. Updated presentation template to new UL Brand
Rev. 4, September 25, 2009
Clarified cover page description of 17025 to indicate 2005 version
Updated Revision History slide to include revisions 1 and 2
Rev. 3, June 23, 2009
Slide 40 – Updated wording from “management system” to “quality management system”
Slide 47 – Corrected document number (00-TC-G0050)
Slide 63 – Remove the bullet referencing DAP job aid 00-OP-J0026
Minor formatting changes throughout for consistency
Rev 2, August 4, 2008
Includes suggestions made by the participants in the "train the trainer" session for CAR Admin Trainers
Rev 1, July 21, 2008
Initial release